## Slide 1: Improving Phosphorus Magnetic Resonance Spectroscopy with Compress Sensing Acceleration, Low Rank reconstruction model, and Artificial Intelligence
Department of Radiology and Medical Informatics, University of Geneva
Julien Songeon
Young Researchers Day 2022
Notes: Welcome to my presentation, I’m attached to the applied physics group but I’m actually doing my research at the Department of Radiology and Medical Informatics at the HUG

## Slide 2: Outline
1. Introduction
    Magnetic Resonance Imaging
    Magnetic Resonance Spectroscopic Imaging
2. Research focuses
    Phosphorus MRS
    Motivation and limitation
3. Current research contribution
    Improvement of data acquisition
    Improvement of data analysis
4. Conclusion
Notes: In this presentation I will start by giving you an introduction on the field, the recherche field of my group and then my contribution.

## Slide 3: 1. Introduction
    Magnetic Resonance Imaging
    Magnetic Resonance Spectroscopic Imaging

## Slide 4: Magnetic Resonance Imaging
A. MRI scanner
Magnetic Resonance Imaging (MRI) is a clinical diagnostic tool.
  Non invasive and non ionizing.
Nuclear magnetic resonance (NMR): the splitting of the spin’s energy level in the presence of a magnetic field (Zeeman effect).
  Magnet field between 1.5T to 7T.
  Spin’s excitation with radio-frequency photons.
1. Introduction
B. Zeeman effect
C. Example of anatomical images
Notes: The MRI is a clinical tool used to obtain anatomical information of the patient. It is based on the NMR and Zeeman effect.
You can see an example of image obtained with an MRI.

## Slide 5: Magnetic Resonance Spectroscopic Imaging
Source: Gajdošík, M. Sci Rep 11, 2094 (2021).
Magnetic Resonance Spectroscopy (MRS).
  Application in-vivo of NMR
  Probes the metabolites concentration.
  Peak amplitude proportional to metabolite concentration.
  Different nuclei can be studied.
Magnetic Resonance Spectroscopy Imaging (MRSI).
  Mapping of the concentration distribution of the metabolites.
  Application for pathologies with abnormalities in metabolic concentration (cancer, stroke epilepsy,…).
1. Introduction
A. Example of spectra for 1H, 31P and 13C
B. Example of MRSI concentration mapping with 1H
Source: Považan, M., NeuroImage vol. 121 126–135 (2015).
Notes: Spectroscopy can be performed with an MR scanner. It is the same as NRM, concentration of metabolites can be obtain as it is directly proportional to the area of the resonance peak. The MR scanner allow the spectroscopy of multiples nuclei.
With MRSI we can obtain a mapping of such concentration with finds clinical application for pathologies with abnormal concentration distribution.

## Slide 6: 2. Research focuses
    Phosphorus MRS
    Motivation and limitation

## Slide 7: Phosphorus MRS
γ-ATP
α-ATP
β-ATP
PCr
Mp
Pi
PE
PCh
GPE
GPC
NAD+ and
NADH
31P-MRS enables detection of high-energy phosphate metabolites
Information on:
  Bioenergy (PCr, ATPs, Pi)
  Cell membrane synthesis (PE, PCh, GPE, GPC)
  pH (chemical shift Pi wrt. PCr)1
  Redox state (NAD+/NADH)2
Method suitable for monitoring tissue function and graft viability for transplantation
  ATP is a sign of mitochondrial function
2. Research focuses
[1] Rudin M. Springer Berlin Heidelberg 1992.
[2] Lijing Xin et al. Frontiers in Nutrition. 2018
A. Example of 31P spectrum obtain with a 3T MRI
Notes: Phosphorus atom is present in molecule linked to the energy metabolism

## Slide 8: Motivation and Limitation
2. Research focuses
Motivations:
  Clinical applications
        Pathologies with abnormal metabolic concentration.
        In-vivo physiology comprehension.
  Application in transplantation
        Phosphorus metabolites provides information on viability of the organ.
        Mapping could improve the organ rejection process.
Limitation:
  Evaluation of overlapping resonances.
  SNR limitations.
  Current algorithms are fitting based. Time-consuming evaluation for 3D mapping
        Requires the evaluations of all voxels.
        With fitting, each spectra needs to have an independent evaluation (few hours for a single organ).
  For high resolutions MRSI, time consuming acquisition.
Notes: Most organs are discarded, but this can be a new diagnostic methods to evaluate the organ quality

## Slide 9: 3. Current research contribution
    Improvement of data acquisition
    Improvement of data analysis

## Slide 10: Improvement of data acquisition
MRI acquires data in the Fourier domain k-space:
  Data need to be Fourier transform to obtain image or spectra.
Compress Sensing (CS) accelerate the acquisition:
  Acquired less data point: k-space random under sampling. Application for:
        Same spatial resolution with a faster acquisition.
        Higher resolution for same acquisition time.
Undersampled k-space cannot be directly Fourier transform to obtain images or spectra
  Regularised reconstruction to interpolate the missing points (Low Rank method).
3. Research contribution
Advantage of the methods:
  Faster acquisition.
  Improved SNR.
Trade off:
  Limited loss of spatial detail
A. Example of k-space under sampling
Source: Klauser A., Magn Reson Med. 2019;81:2841–2857.
Notes: Acquisition can be improved by accelerating the measurement time
CS accelerating the acquisition by under sampling the k-space. Which can be used either for: … …

## Slide 11: Improvement of data analysis
3. Research contribution
31P-Spectral Analysis With Neural Networks: 31P-SPAWNN
Deep Learning approach
  Based on the physical model of metabolites resonances
  Supervised learning with simulation of 106 spectra.
Network trained to estimate
  Metabolites concentrations and spectral parameters (phases, width, baseline, SNR).
Improvement of the methods
  Faster analysis time (few minutes versus few hours).
  Better performance for overlapping resonances.
  Better performance at low SNR.
Source: Songeon J., Magn Reson Med. 2022;
Notes: The data analysis can be improved with artificial intelligence.

## Slide 12: Conclusion
Phosphorus spectroscopy provides unique, non-invasive, cellular information that finds many clinical application.
Compress Sensing and Low Rank reconstruction allow a faster acquisition time.
CNN provides good alternative to traditional lengthy fitting algorithms with
  Improved computation time, much faster for large dataset.
  Robustness at low SNR.
4. Conclusion
Acknowledgement
              Prof. François Lazeyras
              Dr. Antoine Klauser
              Dr. Sebastien Courvoisier
              Oscar Dabrowski
              Dr. Lijing Xin
              Dr. Alban Longchamp
              Thomas Agius
Notes: This brings my conclusion

## Slide 14: 4. Backup slides
Notes: Moving on to the last part of this presentation, we will present our new methods of analysis with artificial intelligence

## Slide 15: Transplantation situation
Source: Swisstransplant annual report 2021
Transplantation is the preferred treatment for end-stage organ disease
Facing a shortage of available organs:
  In 2021, more than 2’100 patients on the Swiss waiting list
  Every year, ~100 people in Switzerland die due to the lack of donors.
Expansion of the donor pool beyond standard-criteria:
  Donation after circulatory death (DCD)
Non-controled period of warm ischemia (pre-existing damage)
  Delayed graft function
        Dialysis for kidney graft
        Poor long-term survival
1. Overview
Notes: Transplantation is the treatment of choice for end-stage organ disease. But we are facing a shortage of available organs, as the number of patients on the waiting list exceeds the number of donors.
There were 3.6 times more patients on the waiting list than transplants performed, with approximately one hundred deaths per year.
One solution would be to expand the donor pool beyond our current standard criteria. In our research we are interested in organs that comes from DCD. There are challenges with those organs as they undergo a period of warm ischemia that can cause …

## Slide 16: Pushing the limit in organ transplantation
Improve organ preservation from ischemia injury
  During ischemia ATP is depleted
  Depletion of ATP trigger a cascade of damage in the mitochondria.
  Once ATP levels have fallen beyond a critical point, the resulting injury is irreversible.
  Current methods of organ preservation is Cold Static Storage (CSS)
        Aim to preserve the energy machinery and reduce the rate of energy depletion
        Hypothermic storage slows but does not entirely suspend cellular metabolism
Creation of a pre-transplant diagnostics
  Creation of a method to assessed organs graft viability
MRI and 31P-MRS to establish organ viability
  In livers, ATP content correlated with transplant outcome1
  The use of biopsy for clinical biochemical ATP analysis is time-consuming, invasive, and costly2
  31P-MRS could assessed ATP and predict kidney energy state, and its viability before transplantation.
Assessment of preservation condition with pig’s kidneys
  Oxygenation effect
  Warm Ischemia impact on organ
  Sub-normothermic machine perfusion
1. Overview
[1] Amundsen et al. Transplantation. 2017
[2] Bruinsma et al. Scientific Reports. 2016
Notes: In order to transplant DCD organs, we need to improve the organ preservation from ischemia injury and we need to have a pre-transplant diagnostic.
What we know about ischemia injury is that ATP is depleted, the injury will create a cascade of damage in the mitochondria and once the energy level of the mit. fall under a certain threshold the injury is irreversible.
Read second and third bullet point.
Which is why we aim to use the MRI to assess the ATP as we all know that MRI it is a non-invasive tool.

## Slide 17: MRI protocol
MR compatible perfusion machine
MR compatible machine5
  Perfusion performed continuously during MRI and MRS acquisition
  Isothermal box with temperature maintenance
Controle module
  Is left in the control room, and connected to the perfusion module with the umbilical cord
  Pressure monitoring pO2, Temperature, Alarms
31P MRS
  Single-loop coil placed at the bottom of the tank text
        Matrix size 16x16x8, spatial resolution of 15.6x15.6x20 mm3
        Quantification using Inorganic phosphate (Pi) with known 25mM concentration in the buffer.
2. MRI methods
[5] Longchamp et al. Transplantation. 2020
Notes: Here are pictures of our MR compatible perfusion machine.

## Slide 18: Benefit of Oxygenation
Oxygenation needed
  Ability of kidney to generate ATP relies on sufficient oxygenation
  In absence of O2, ATP is hydrolysed into ADP and mainly AMP (present in PME).
  After reperfusion with O2, cells rephosphorylate AMP into ATP if the cells are still alive.
Hypothermic pulsatile perfusion with a fixed pO2 of 110 kPa
  Consumption of PME to maintain ATP concentration levels5
2. MRI methods
γ-ATP
α-ATP
β-ATP
PME
γ-ATP
α-ATP
β-ATP
PME
NAD+ and
NADH
O2 ON
O2 OFF
O2 ON
A
B
C
[5] Longchamp et al. Transplantation. 2020
Notes: There is a need of oxygenation in order to generate ATP
Under oxygenation, you will have a slow consumption of AMP to maintain ATP concentration level

## Slide 19: Impact of Warm Ischemia
Warm Ischemia (WI)
  Many DCD grafts are discarded because of long warm ischemia times
  Absence of reliable measure of kidney viability
  Consensus threshold at 30 minutes of WI
Results5
  Lower level of ATP at 60 minutes of WI
  Higher Histological damages score at 60 minutes of WI
  Correlation of ATP concentration with Histological score
        ATP can be use as to estimate the cellular damage
2. MRI methods
[5] Longchamp et al. Transplantation. 2020
Notes: We also investigated the impact of warm ischemia.
The organ will be exposed to warm ischemia in DCD condition
This suggests that we can use the ATP level concentration to estimate cellular damage and the overall organ viability

## Slide 20: Sub-NormothermiA
Sub-normothermia
  Investigate if it improves:
        Reduction of Ischemia-Reperfusion Injury
        Kidney metabolism with ATP production
  3 groups: Hypothermia at 4°C without or with oxygen (HMP or HMOP) and Sub-normothermia at 22°C with oxygen (SNOP)
Results6
  Higher ATP levels before and after transplantation
  Good correlation with histological score results with lower injuries in Sub-normothermia
        Injuries effect occurs during and after reperfusion
Organ preservation with a 22°C perfusion
2. MRI methods
E
F
[6] Songeon et al. Accepted for publication in Transplantation Direct.
.
Notes: One of the disadvantage of CSS is that organ are subjects of IRI when retransplanted. Going from a slow metabolism at low temperature to a nominal speed metabolism at body temperature
We expect higher ATP levels in pre as the metabolism is not slowed and maintain its activity
The conclusion is that injuries occurs after reperfusion and 22°C help improve the reduction of the injury. Which we can again correlate with ATP levels
With the interest in ATP, we want to have a methods of evaluation for 31p spectroscopy

## Slide 21: Evaluation with Neural Networks
Deep Learning approach
  Based on a physical model
        Metabolites resonances
        Sequence (FID)
  Supervised learning
        Simulation of 106 to train the network
Network trained to estimate
  Metabolites concentrations
  Spectral parameters
        0th and 1st order phases, chemical shift, lorentzian and gaussian width, baseline and SNR
3. Artificial Intelligence
31P-Spectral Analysis With Neural Networks: 31P-SPAWNN
[7] Songeon, et al. Accepted for publication in Magnetic resonance in Medecine
Notes: Huge advantage for supervised learning

## Slide 22: Evaluation with Neural Networks
Convolutional Neural Network
  Two different CNN architectures
        LeNet based for parameter and concentration quantification
        U-Net for baseline estimation
3. Artificial Intelligence
31P-Spectral Analysis With Neural Networks: 31P-SPAWNN
Parameter and concentration evaluation
Baseline evaluation
[7] Songeon, et al. Accepted for publication in Magnetic resonance in Medecine

## Slide 23: Evaluation with Neural Networks
3. Artificial Intelligence
Reconstruction
  We can reconstruct the spectrum using the physical models with the parameters and concentration values obtained with the evaluation
  The reconstruction is not to be confused with a fitting
High accuracy and robustness especially in low SNR
Fast computation time
  Training a NN takes about 4h-5h but needs to be done only once
  Once training done, the evaluation takes 5 minutes for a full 10x10x10 MRSI matrix vs 1h for LCModel
[7] Songeon, et al. Accepted for publication in Magnetic resonance in Medecine
Notes: 3d MRSI on a volunteer brain, with the exemple of evaluation of 2 voxels
NN evaluate spectrum, return a set of values (concentration, parameters) and we use these values to create a spectrum with our physical model.
Overlay on top of invite data
adventage in clinical settings

## Slide 24: Futur work: aim at nad+/nadh 3t
3T
7T
3. Artificial Intelligence
5Hz
15Hz
Redox state
  Information of oxidative stress with the imbalance of free radical activity and antioxidant activity
  Suspected to be important in neurodegenerative pathology
Estimation of Redox state at 7T
  Mitochondrial NAD+/NADH Redox State4
  Better definition of the multiplet structure of NAD+ even with a broad linewidth
Estimation at of redox state using Artificial Intelligence
  Combined the AI at 3T with the higher resolution and SNR with the futur 7T
  In parallel, develop further the AI at 3T
NAD+
NADH
15Hz
[4] Lijing Xin et al. Frontiers in Nutrition. 2018
Notes: For my last slide I want total about our futur work

## Slide 25: Backup slides
3. Artificial Intelligence

## Slide 26: Backup slides
3. Artificial Intelligence